## Slide 1
PROTEUS · SDN INTRUSION-DETECTION RESEARCH
What an SDN Controller Can Actually Observe
A measurement and validity study of the InSDN OpenFlow control channel
Adhyan Jain · Atharva Sheersh Pandey · Kshitij Manikshete VIT Vellore

## Slide 2
THE PROBLEM
Detectors are scored on data the controller never sees
• SDN papers say the controller has a global view, so build the detector there.
• But they test on CSV features computed at the victim host, then call it controller-based.
• Nobody checked what the controller actually receives.
• InSDN also recorded its controller's OpenFlow traffic. We opened those recordings.

## Slide 3
APPROACH
What we did: 44 recordings, three questions
• Q1 Can the controller see the flows the dataset labels?
• Q2 Does what it sees depend on the forwarding app? (Mininet + Ryu, 65 runs)
• Q3 Is a high score on the controller's view proof of detection?
Data: 44 InSDN controller captures (11 benign, 33 attack) + our own Mininet/Ryu testbed

## Slide 4
GAP IN THE BENCHMARK
Novelty 1 · The controller never saw the labelled flows
0 of 3,827
FlowMods carry IP addresses or ports
91
FlowMods from Ryu's stock app: also MAC-pair only
• The dataset labels 5-tuple flows; the controller's rules only matched MAC pairs or EtherType.
• So CSV-trained detectors are not controller-side detectors.

## Slide 5
MEASURED EFFECT
Novelty 2 · The forwarding app decides what the controller sees
Chart: 
| MAC-pair | Per-flow
v | 12.3 | 10422
TCP PacketIns per run (1 switch, 10 runs)
• Same traffic: 847x more PacketIns with per-flow rules.
• Holds on a 3-switch chain too.
• A 2 s idle timeout hides most per-flow entries from a 1 s poller (153 to 37).

## Slide 6
VALIDITY
Novelty 3 · A high score is not proof of detection
Chart: 
| PacketIn-rate threshold | MLP | Trivial rule: any IP PacketIn
v | 0.61628 | 0.94579 | 0.99531
Balanced accuracy, unseen captures, 1 s windows
• A one-line rule beats the model inside attack sessions.
• InSDN records benign and attack in separate sessions, so scores may reflect the session.
• Fix: benign and attack traffic mixed in one session.

## Slide 7
FOUR PAPERS, ONE FULL TEXT READ
How published InSDN results compare
• Early Detection of Intrusion in SDN: Random forest 98.84% vs LSTM 85.31%
• Intrusion detection in software defined network using deep learning approaches: Transformer 99.02%
• A Hybrid CNN-LSTM Based Approach for Anomaly Detection Systems in SDNs: 96.32% accuracy
• Securing IoT and SDN systems using deep-learning based automatic intrusion detection: 99.73% accuracy, 98.6% detection rate
• Towhid et al. (full text read): 9 packet-derived features, all flows split 70:30, no grouping by capture or session mentioned.
• Our test, same classifier: random flow split 0.9998; held-out source hosts 0.907 ± 0.085; IPs and ports alone 1.000.
• Claimed: a random split overstates the score for unseen hosts by about 9 points. Not claimed: their exact numbers are wrong.

## Slide 8
METHOD
Novelty 4 and 5 · A caught pitfall, a rerunnable package
• Our first test app let ping/ARP rules hide TCP: the effect looked like 4x instead of about 847x. We report both.
• Overlapping coarse rules can understate controller load by two orders of magnitude.
• One command rebuilds every result from hashed captures and checks the paper's numbers.

## Slide 9
PIPELINE
Study architecture: what goes in, what comes out
A · InSDN captures (recorded, offline)
44 pcaps
in: ONOS TCP 6653
Parser
out: PacketIn, FlowMod, stats
Labels
CSV flow IDs → tag per PacketIn
Windows
22 features per 1–5 s
History
88 inputs
Models + tests
10 seeds, CI, trivial rule
B · Live forwarding study (no InSDN data)
Ryu app
3 forwarding modes
Mininet
1 or 3 switches, benign traffic
Control-channel pcap
one per run
Counts per mode
PacketIn, FlowMod, entries
Both end as results/*.json → tables in the paper
model input: 88 numbers about a few seconds of controller messages · output: attack / not attack per window · the CSV only supplies labels

## Slide 10
HONEST SCOPE
What is not new, what we did not do, what is next
Not new
• Control-plane telemetry for SDN IDS (LAN-SDN-NIDS, SDNFLow)
• The detector itself
• Stock Ryu behaviour
Not done
• Benign + attack in one session
• OpenDaylight or another dataset
• A re-implemented published detector
Next
• Interleave benign and attack traffic
• Gap on a second controller family
• In-fold oversampling for rare classes
Venue: workshop / conference as is; lower-quartile journal after revision.

## Slide 11
CONTEXT
The earlier Proteus system: a prototype, not a claim
• Built: WGAN-GP synthetic attacks, KS drift test, MMD fidelity gate, drift-triggered retraining, versioned releases.
• Close prior work exists (NetGuard 2025: generative adaptation for drifting, imbalanced IDS data).
• Our own studies found no benefit from the generative step; the demo's gain came from oracle labels.
• So the research contribution is the InSDN study; Proteus is kept as context (/old console).

## Slide 12
CLOSE
Takeaways
• The controller's rules never contained the labelled 5-tuples.
• What a controller sees depends on the forwarding app.
• On InSDN, controller-side scores are not detection accuracy.
Next: interleave benign and attack traffic in one session; test a second controller.